### FLYBACK PRACTICAL DESIGN EXAMPLE

#### SWITCHING POWER SUPPLY SPECIFICATION

1. INPUT:

1.1 VOLTAGE:			UNIVERSAL AC 90V-AC260V SINGLE PHASE.

1.2 FREQUENCY:		47Hz-63Hz.

1.3 RMS CURRENT:	2A Max.

1.4 INRUSH CURRENT:	30A Max. WHILE COLD START AT PEAK ON

FULL LOAD, 25℃ AMBIENT.

1.5 EFFICIENCY:		70% Min. AT NOMINAL LINE INPUT, FULL LOAD.

2. OUTPUT:

2.1 DC OUTPUT:

| Voltage | 15.0V |
| --- | --- |
| MAX. Load | 2.0A |
| MIN. Load | 0.1A |
| Regulation | +/- 5% |
| Ripple & Noise | 150mV |

NOTE:  FOR RIPPLE & NOISE MEASUREMENT, USE A 20 MHz

BANDWIDTH FREQUENCY OSCILLOSCOPE, AND ADD 0.1uF

MULTILAYER CAPACITOR AND A 22uF ELECTROLYTIC

CAPACITOR AT OUTPUT CONNETCTOR TERMINAL

3. TIME SEQUENCEE:

3.1 RISE TIME: 70mS Max. AT NOMINAL LINE VOLTAGE, FULL LOAD.

3.2 TURN-ON DELAY TIME: 1000mS Max. AT NOMINAL LINE VOLTAGE

FULL LOAD.

3.3 HOLD-UP TIME: 20mS Min. AT 230Vac/50Hz INPUT, 16ms Min. AT

115Vac/60Hz INPUT. FOR OUTPUT, AT FULL LOAD

4. PROTECTION:

4.1 OVER VOLTAGE PROTECTION: OVP AT 110-140%

4.2 SHORT CIRCUIT PROTECTION:

THE OUTPUT WITHSTAND AN INDEFINITE SHORT CIRCUIT

WITHOUT DAMAGE TO THE POWER SUPPLY

4.3 OVER POWER PROTECTION:

WHEN OUTPUT POWER EXCEEDS 110%-160% OF RATED LOAD,

THE POWER SUPPLY WILL SHUT DOWN.

4.3 WHEN PROTECTION CIRCUIT IS WORKING, THE POWER SUPPLY

WILL SHUT DOWN. ONCE THE ABNORMAL CONDITIONS ARE

REMOVED, THE POWER SUPPLY WILL RESTART AUTOMATICALLY.

5. SAFETY REQUIREMENT:

5.1 THIS POWER SUPPLY IS DESIGNED TO MEET FOLLOWING

STANDARDS:

1) UL 1950.

2) CSA 22.2 NO. 0-M1982; BULLETIN 1402C.

3) IEC 950

5.2 DIELECTRIC WITHSTAND:

1) PRIMARY TO SECONDARY: 1500Vac FOR 1 MINUTEE.

2) PRIMARY TO SAFETY GROUND: 1500Vac FOR 1 MINUTE.

5.3 LEAKAGE CURRENT: 3.5mA Max. AT 245 Vac

6. CONDUCTED EMI REQUIREMENT:

1) FCC DOCKET 20780, PART 15, SUBPART J, CLASS B.

2) BZT Vfg 243/1991 CLASS B.

7. ENVIRONMENT:

7.1 OPERATING TEMPERATURE : 10℃TO 50℃.

7.2 OPERATING RELATIVE HUMIDITY: 20% TO 90%.

7.3 STORAGE TEMPERATURE : -20℃ TO 60℃.

7.4 STORAGE RELATIVE HUMIDITY: 10% TO 90%.

7.5 COOLING: SHOULD OPERATE

WITHOUT FAN

FLYBACK DESIGN THEORY:

Considering Power MOSFET Vds stress is safe, and current level capacity is enough.

Decide turn ratio by

The maximum duty D

Pout=1/2 Lp*Ipp2*f

Vinmin=Lp*Ipp*f/D

Ip=2*Pout/(Vinmin*Dmax)

Lp=VinminDmax/(Ipp*f)

DETERMINE DCM/CCM BOUNDARY

IOB=Io(max)*(X% PERCENTAGE)

Vdc(BOUNDARY)=Vdc

DECIDE DUTY CYCLE AND CALCULATE TURN RATIO

WHERE N : TURN RATIO Np/Ns

D(max) : MAX. DUTY CYCLE

Vdc(min)=MIN. DC VOLTAGE

Vo : OUTPUT VOLTAGE

Vf : DIODE FORWARD VOLTAGE DROP

IF N IS DECIDED, THEN RECKECK D(max)

DETERMINE SECONDARY PEAK CURRENT IN DCM/CCM

DECIDE SECONDARY WINDING INDUCTAANCE Ls

DECIDE PRIMARY WINDING INDUCTANCE Lp in CCM

For energy transfer,

And,

Therefore,			*(1/Krp)

Lp = N2Ls

DETERMINE SECONDARY PEAK CURRENT IN CCM

Wave form factor Krp :

Peak current Ipeak (Ip):

Ripple current ΔI:

RMS current Irms:

Bac =Krp * Bmax

DETERMINE PRIMARY PEAK CURRENT IN CCM

Loss allocation factor Z		Z=0.5~0.7

CALCULATE APPARENT POWER

DECIDE CORE SIZE

(1+K) Bmax + Br < Bsat			Set K=0.2;		Bac=0.5*Bsat

Ac*Ae=(25.32*Lp*Ipp*d*d)/Bmax

WHERE Wa : WINDOW AREA, cm2

Ae : EFFECTIVE CROSS-SECTIONAL AREA, cm2

Ku : WINDING FACTOR, 0.2-0.5

J : CURRENT DENSITY, A/cm2

Fs : OPERATING FREQUENCY, Hz

Bm : Magnetic flux density , T

Pt : total power including output and input power

CALCULATEE PRIMARY TURNS Np:

DETERMINE AIR GAP

CALCULATTE SECONDARY TURNS Ns

CALCULATE AUXILIARY WINDING TURNS NA

DETERMINE WINDING WIRE SIZE

WHERE Aw : WIRE AREA; cm2

DESIGN THEORY

CONSIDER DRAIN-SOURCE BREAKDOWN VOLTAGE BVDSS

(COLLECTOR-EMITTER BREAKDOWN VOLTAGE BVceo)

BVDSS (BVceo) > Vdc(max) + N(Vo+Vf)

CONSIDER CONTINUOUS DRAIN CURRENT ID

(D.C. COLLECTOR CURRENT Ic)

CONSIDER PULSED DRAIN CURRENT IDM(PEAK COLLECTOR CURRENT Ic(peak))

CONSIDER MOSFET STATIC DRAIN-SOURCE ON-STATE RESISTANCE

RDS(ON) [TRANSISTORR COLLECTOR SATURATION VOLTAGE Vce(sat)]

# DESIGN THEORY

CONSIDER REPETITIVE PEAK REVERSE VOLTAGE VRRM

CONSIDER AVERAGE OUTPUT RECTIFIED CURRENT Io(avg)

Io(avg) > Io(max)

CONSIDER NON-REPETITIVE PEAK SURGE CURRENT IFSM

### DESIGN THEORY

CALCULATE OUTPUT CAPACITANC

CHOOSE CAPACITOR RATED VOLTAGE	W.V. > 1.2*Vo

CALCULATE R.M.S. RIPPLE CURRENT

CALCULATE E.S.R. OF CAPACITOR

FLYBACK DESIGN EXAMPLE

[DESIGN ENVIROMENT RATING]

CONDITION: Po=30W,	     EFF=0.7,P.F.=0.6, Vac(min)=90V

Vin:         Bmax    Iin:     D:   Pout:

Circuit Topology

Transformer Electrical Diagram

Minimum Working AC input Voltage		VACMIN		Volts

Minimum Working DC input Voltage		VDCMIN		Volts

Maximum Working AC input Voltage		VACMAX		Volts

Maximum Working DC input Voltage		VDCMAX		Volts

AC Mains Frequency Range			FAC		Hertz

Bridge Rectifier Conduction Time Estimate	TC		mSeconds

Input Bulk Filter Capacitor			CIN		uFarads

PWM Switching Frequency Range		FS		Hertz

Permit Maximum Operation Duty		D		%

Voltage Regulation				VR		%

Output Voltage				VO(n)		Volts

Output Rectifier Diode Forward Voltage Drop	VD		Volts

Output Current				Io(n)		Amperes

Output Power				Po(n)		Watts

Switch on-state Drain to Source Voltage 		VDS		Volts

Efficiency Estimate				EFF		%

Loss Allocation Factor 			LAF

Safety Class				CLASS

[FUSE DESIGN SECTION]

Max. INPUT CURRENT

BECAUSE THEE ADAPTOR IS UNIVERSAL INPUT

CHOOSE 250V VOLTAGE RATING FUSEE

IF THE MAX INRUSH CURRENT IS 12A, TIME DURATION IS 10mS,

THEN

[Ii2t] = (12)2 * (10 * 10-3) =1.44

IF WE CHOOSE 1A FUSE OF "2AG FAST-ACTING" TYPE, THEN FROM

CURRENT-TIME CHART WE CAN GET THE CURRENT ABOUT 8A IN

THE 10mS CONDITION. THEREFORE, THE ENERGY IS

[Ii2t] = (9)2 * (10 * 10-3) =0.81

BECAUSE [I2t] < [Ii2t], SO WE CAN NOT USE THIS TYPE FUSE.

CHOOSE ANOTHER 1A FUSE OF "2AG SLOW-BLOW" TYPE, THEN WE

CAN GET THE CURRENT ABOUT 23A IN TTHE 10mS CONDITION.

THEREFORE, THE ENERGY IS

[Ii2t] = (23)2 * (10 * 10-3) =5.29

IF THE THERMAL AGEING COEFFICIENT "A" IS 0.3, THEN

A[I2t] = 0.3 * 5.29 = 1.59

SO

A[I2t] > [Ii2t]     WE CAN CHOOSE THIS TYPE FUSE.

[NTC DESIGN SECTION]

CONDITION : Po=30W, η=0.7, PF=0.6, Vac(spec) = 230V,

Vac(min)=90V

ZERO POWER RESISTANCE RT

MAXIMUM PERMISSIBLE CURRENT IT

THEREFORE, WE CHOOSE "UEI" NTC THERMISTORR

"N10SP010", WHICH

RT=10 (OHM)

IT=3.0A

[RECTIFIER DESIGN SECTION]

MAX. DC BLOCKING VOLTAGE

MAX. AVERAGE FORWARD RECTIFIED OUTPUT CURRENT

CHOOSE RS105 BRIDGE DIODE 1A/600V

[BULK CAPACITOR DESIGN SECTION]

CAP.VALUE

=67.6μF

RIPPLE CURRENT

WORKING VOLTAGE

CHOOSE 68uF/400V RUBYCON USP SERIES

[VARISTOR DESIGN SECTION]

[X’FM DESIGN SECTION]

# PRACTICAL DESIGN

WINDING AREA ALLOCATION FACTOR 1:3

Core Type				Core

Bobbin Type				Bobbin

Core Saturated Flux Density 100℃		BS		Tesla

Core Rest Flux Density 100℃			BR		Tesla

Core Effective Cross Sectional Area		AE		cm^2

Core Effective Path Length			LE		cm

Core Volumn/Weight			VC		cm^3

Core Loss Density				Pb		Watts/cm^3

Ungapped Core Effective Inductance		AL		nH/T^2

Bobbin Effective Widing Area			AC		mm^2

Bobbin Physical Winding Width		BW		mm

Safety Margin Width 			MW		mm

Frenquency Range				F		Hz

ui

He		A/m

CHOOSE CORE MATERIAL

FERRITE----------Mn-Zn

EFFECTIVE SATURATION MAGNETIC FLUX DENSITY Bsat 5000 Gauss

CHOOSE CORE MANUFACTORY AND FERRITE MATERIAL

- TDK------PC30, PC40

- THOMSON------B50

- TOMITA------2E6

- FUJI------H45

- TOKIN------2500B, 2500B2

- SIEMENS------N27, N67, N87

- MAGNETICS------R, P, F MATERRIAL

- FERROXCUBE------3B7, 3C8

- SATCKPOLE------24B

- INDIANA GENERAL------

- NIPPON FERRITE------SB-5S, GP-5, GP-7

- 川鐵------MB-3

- HITACHI------SB7C, SB9C

- PHILIPS------3C80, 3C85, 3F3

- NIPPON CERAMIC------NC-1M, NC-2M

- MITSUBISHI------NZ, NK, NA, NX

- SAM HWA------SB-5S, GP-5, GP-7

CHOOSE CORE TYPE

1.  EI TYPE                5.  LP (FQK) TYPE

2.  EE TYPE                6.  RM TYPE

3.  EER TYPEE             7.  EPC TYPE

4.  PQ TYPE               8  .ETD (EC) TYPE

CONDITION : Po=30W, Fs=40KHz,η=0.7,Vo=15V,Io=2A

DCM/CCM BOUNDARY

IOB = Io(min) = 65%*Io(max)

= 0.65*2 =1.3A

Vdc(BOUNDARY)=100Vdc

MAX. DUTY CYCLE AND TURN RATIO

ASSUME Dmax = 0.45

RECHECK D(max)

IN DCM / CCM    △IsB SECONDARY PEAK CURRENT

Ip=2*Pout/Vinmin*Dmax

Lp=Vinmin*Dmax/(Ipp*f)

DECIDE Ls

DECIDE Lp

Lp = N2Ls = (5)2*48.28

=1.207mH

IN CCM △Isp SECONDARY PEAK CURRENT

IN CCM △Ipp PRIMARY PEAK CURRENT

APPARENT POWER Pt

CORE SIZE

Ku =0.6

Ac*Ae=6.33*Lp*Ipp*d*d/Bmax/Ku

CHOOSE EER-28 JPP-4 FERRITE CORE,

CORE DATA AS FOLLOWING :

Ae: 85.4mm2   Ac:141.25mm2   Ve=6353.8mm3	 Ac*Ae=1.206cm4

PRIMARY TURNS Np

SECONDARY TURNS Ns

AUX. WINDING TURNS NA

WINDING WIRE SIZE

[POWER MOSFET DESIGN SECTION]

DRAIN-SORCE BREAKDOWN VOLTAGEE BVDSS

BVDSS > Vdc(max) + N(Vo+Vf)=360+5*(15+1)=435V

CONTINUOUS DRAIN CURRENT ID

PULSED DRAIN CURRENT IDM

CHOOSE 2SK118 MOSFET (TOSHIBA), THE RATING ARE :

BVDSS (VDSS) = 600V               ID=6A

IDM (IDP) = 24A                    RDS(ON)=0.95(OHM)

[OUTPUT DIODE DESIGN SECTION]

REPETITIVE PEAK REVERSE VOLTAGE VRRM

AVERAGE OUTPUT REECTIFIED CURRENT Io(avg)

Io(avg) > Io(max) = 2A

NON-REPETITIVE PEAK SURGE CURRENT IFSM

CHOOSE BYQ28-100 ULTRA FAST-RECOVERY DIODE (PHILIPS)

VRRM=100V                   Io(avg)=10A (TWO DIODE)

IFSM=50A                     VFM=0.85V

[OUTPUT CAPACITOR DESIGN SECTION]

OUTPUT CAPACITANCE

CHOOSE 2200uF

CAPACITOR RATED VOLTAGEE

W.V. > Vo = 15V

CHOOSE RATED VOLTAGE 25V

R.M.S. RIPPLE CURRENT

CHOOSE RUBYCON YXB SERIES CAPACITOR 2200uF/25V,

THE RIPPLE CURRENT IS

Iripple(rms)=1.646A (AT 105℃ ,100KHZ)

BUT IN 85℃ , 50KHZ, THE R.M.S. RIPPLE CURRENT IS

Iripple(rms)=1.646*1.7*0.89=2.74A

WHICH CAN SATISFY THE ABOVE REQUIREMENT

E.S.R. OFF CAPACITOR

2200uF/16       ESR=29m (OHM)

CAN NOT SATISFY THE REQUIREMENT, MUST ADD ANOTHER

LC FILTER

DECIDE Lc FILTER

ASSUME

IF CHOOSE Lf = 10uH, THEN

CHOOSE Cf = 1000uF / 16V

[OUTPUT REGULATION DESIGN SECTION]

[OUTPUT PROTECTION DESIGN SECTION]

[PWM CONTROLER IC DESIGN SECTION]

[FEEDBACK LOOP GAIN DESIGN SECTION]

[THERMAL DESIGN SECTION]

[EMC FILTER DESIGN SECTION]

APPENDIX

|  |  |  | Area |  | Amps | Amps | Amps | Amps | Amps | Amps | Amps | Amps |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AWG Size | mm | mm | (mm2) |  | 3A/mm2 | 4A/mm2 | 5A/mm2 | 6A/mm2 | 7A/mm2 | 8A/mm2 | 9A/mm2 | 10A/mm2 |
| 12 AWG | 2.052 | 2.052 | 3.3071 |  | 9.921 | 13.228 | 16.535 | 19.842 | 23.150 | 26.457 | 29.764 | 33.071 |
| 13 AWG | 1.829 | 1.829 | 2.6273 |  | 7.882 | 10.509 | 13.137 | 15.764 | 18.391 | 21.019 | 23.646 | 26.273 |
| 14 AWG | 1.928 | 1.928 | 2.9195 |  | 8.758 | 11.678 | 14.597 | 17.517 | 20.436 | 23.356 | 26.275 | 29.195 |
| 15 AWG | 1.450 | 1.450 | 1.6513 |  | 4.954 | 6.605 | 8.256 | 9.908 | 11.559 | 13.210 | 14.862 | 16.513 |
| 16 AWG | 1.291 | 1.291 | 1.3090 |  | 3.927 | 5.236 | 6.545 | 7.854 | 9.163 | 10.472 | 11.781 | 13.090 |
| 17 AWG | 1.150 | 1.150 | 1.0387 |  | 3.116 | 4.155 | 5.193 | 6.232 | 7.271 | 8.310 | 9.348 | 10.387 |
| 18 AWG | 1.024 | 1.024 | 0.8235 |  | 2.471 | 3.294 | 4.118 | 4.941 | 5.765 | 6.588 | 7.412 | 8.235 |
| 19 AWG | 0.912 | 0.912 | 0.6533 |  | 1.960 | 2.613 | 3.266 | 3.920 | 4.573 | 5.226 | 5.879 | 6.533 |
| 20 AWG | 0.813 | 0.813 | 0.5191 |  | 1.557 | 2.076 | 2.596 | 3.115 | 3.634 | 4.153 | 4.672 | 5.191 |
| 21 AWG | 0.724 | 0.724 | 0.4117 |  | 1.235 | 1.647 | 2.058 | 2.470 | 2.882 | 3.293 | 3.705 | 4.117 |
| 22 AWG | 0.643 | 0.643 | 0.3247 |  | 0.974 | 1.299 | 1.624 | 1.948 | 2.273 | 2.598 | 2.922 | 3.247 |
| 23 AWG | 0.574 | 0.574 | 0.2588 |  | 0.776 | 1.035 | 1.294 | 1.553 | 1.811 | 2.070 | 2.329 | 2.588 |
| 24 AWG | 0.511 | 0.511 | 0.2051 |  | 0.615 | 0.820 | 1.025 | 1.231 | 1.436 | 1.641 | 1.846 | 2.051 |
| 25 AWG | 0.455 | 0.455 | 0.1626 |  | 0.488 | 0.650 | 0.813 | 0.976 | 1.138 | 1.301 | 1.463 | 1.626 |
| 26 AWG | 0.404 | 0.404 | 0.1282 |  | 0.385 | 0.513 | 0.641 | 0.769 | 0.897 | 1.026 | 1.154 | 1.282 |
| 27 AWG | 0.361 | 0.361 | 0.1024 |  | 0.307 | 0.409 | 0.512 | 0.614 | 0.716 | 0.819 | 0.921 | 1.024 |
| 28 AWG | 0.320 | 0.320 | 0.0804 |  | 0.241 | 0.322 | 0.402 | 0.483 | 0.563 | 0.643 | 0.724 | 0.804 |
| 29 AWG | 0.287 | 0.287 | 0.0647 |  | 0.194 | 0.259 | 0.323 | 0.388 | 0.453 | 0.518 | 0.582 | 0.647 |
| 30 AWG | 0.254 | 0.254 | 0.0507 |  | 0.152 | 0.203 | 0.253 | 0.304 | 0.355 | 0.405 | 0.456 | 0.507 |
| 31 AWG | 0.226 | 0.226 | 0.0401 |  | 0.120 | 0.160 | 0.201 | 0.241 | 0.281 | 0.321 | 0.361 | 0.401 |
| 32 AWG | 0.203 | 0.203 | 0.0324 |  | 0.097 | 0.129 | 0.162 | 0.194 | 0.227 | 0.259 | 0.291 | 0.324 |
| 33 AWG | 0.180 | 0.180 | 0.0254 |  | 0.076 | 0.102 | 0.127 | 0.153 | 0.178 | 0.204 | 0.229 | 0.254 |
| 34 AWG | 0.160 | 0.160 | 0.0201 |  | 0.060 | 0.080 | 0.101 | 0.121 | 0.141 | 0.161 | 0.181 | 0.201 |
| 35 AWG | 0.142 | 0.142 | 0.0158 |  | 0.048 | 0.063 | 0.079 | 0.095 | 0.111 | 0.127 | 0.143 | 0.158 |
| 36 AWG | 0.127 | 0.127 | 0.0127 |  | 0.038 | 0.051 | 0.063 | 0.076 | 0.089 | 0.101 | 0.114 | 0.127 |
| 37 AWG | 0.114 | 0.114 | 0.0102 |  | 0.031 | 0.041 | 0.051 | 0.061 | 0.071 | 0.082 | 0.092 | 0.102 |
| 38 AWG | 0.102 | 0.102 | 0.0082 |  | 0.025 | 0.033 | 0.041 | 0.049 | 0.057 | 0.065 | 0.074 | 0.082 |
| 39 AWG | 0.089 | 0.089 | 0.0062 |  | 0.019 | 0.025 | 0.031 | 0.037 | 0.044 | 0.050 | 0.056 | 0.062 |
| 40 AWG | 0.079 | 0.079 | 0.0049 |  | 0.015 | 0.020 | 0.025 | 0.029 | 0.034 | 0.039 | 0.044 | 0.049 |

附件1

附件2