- Scope

This specification give data about power supply usable to charge 40 cells alcaline batteries

(碱性电池).

- Technical data

Power: 100w

Output voltage:65v+/-0.5v

Output current:1.5a+/-0.1a

Current ripple:<30%

Input voltage:90 to 132vac

Temperature range:-20℃ to +70℃

The power supply will be used as a current generator 30v until 65v.

The current load will be constant current or pulsed current with duration

0.1s and variable periods .

The current overshoot at beginning of pulse must be less than 0.03As.

The voltage overshoot must be less than 5v.

The output characteristics will be:

3 Standards

Safety compliant with UL,CSA and Telecom standard

EMC compliant with UL,CSA and Telecom standard

4 Protections

Protection against internal short-circuit

Protection against output short-circuit

Protection against wrong polarity

Protection against overheating

5 Plug

2 pins IEC 320 or 3 pins IEC320 connector

6 Output connector

To be confirmed

7 Dimensions

As small as possible :<35ⅹ75ⅹ130mm

# Text boxes

Current

overshoot

0.1s

Max

current

0A

Current

Voltage

overshoot

Max

voltage

Max voltage/2 at

least

0.2s to 4s

Voltage

65v

Voltage

30v

0A

1.5A

Current