## Resistance and Ohm's law

For any piece of conducting material connected to a voltage difference, V, which drives through it a current I, we define the  resistance of the conductor to be 

Many of you are probably more familiar with this relation in the form

and you are used to calling this  Ohm's law.  Everybody does this, but it is technically incorrect;  this is really just the definition of resistance.

## 1  The Definition of Resistance

In electrical circuits, resistance is denoted R and is defined to be the slope of the voltage-versus-current curve, whenever that is well-defined. In symbols,

| R := | ∂V ∂I | ¦ ¦ ¦ ¦ | G.C. | (1) |
| --- | --- | --- | --- | --- |

where G.C. stands for Given Conditions, which is horribly open to interpretation, as discussed below. The unit of resistance is the ohm, defined to be one volt per amp.

Under a wide range of practical conditions, metallic wires and some other circuit elements exhibit a voltage drop ΔV proportional to the current I, in which case equation 1 simplifies to

| R = | ΔV I | (2) |
| --- | --- | --- |

which is called Ohm’s law. Both sides of this equation have an implicit dependence on the Given Conditions, as will be discussed below.