Specifications for Charger of 42V/5A

| Model |  |
| --- | --- |
| Max. Output Power/Nominal Voltage | 210Watt / 42Volt |
| AC Input | Input Voltage | Single Phase |
|  |  | AC110V / AC220V |
|  | Frequency | 50/60 Hz |
|  | Input Current | ?A |
| DC Output | Charging Mode | Two-stage charging (CC/CV) |
|  | Output Voltage | 41.5V +/- 0.15V |
|  | Output Current | 5A +/-0.1A |
|  | Termination Current | 500mA +/-100mA |
|  | Current Ripple | ?? |
| Efficiency | ?? |
| Protective Function | Reverse Charging Protection | Yes |
|  | Short circuit protection | Yes |
|  | Over temperature protection/ Power reduction | Yes |
|  | Output connection open | Yes |
| LED Display | ? |
| Connector /Lines | Input socket | IEC 320 C14 Inlet |
|  | Output pin | 1 : POS, 2 : NEG, 3 : Ground Or with your suggestion |
| Cooling | FAN cooling |
| Operating Temperature | -20ºC ~ +40ºC |

请注意：（１）红色标示部分为重要的指标，不可协商或修改．其他参数和要求可以协商．

（２）在保护功能中突出强调极性反接保护和反向充电禁止．即，当电池组接入充电器的极性发生反接的错误时，应自动停止充电，同时电池组不能向充电器反向充电或反向放电．

（３）联系电话：０７５５－８６０６９２７７　传真：０７５５－８６０６９２６４

１３３８０３４５８１８

电子邮件：szduj@126.com