| CD286 SERIES |  |
| --- | --- |
| Load life of 2000 hours at 105℃ Switch power supply |  |

- SPECIFICATIONS

| Item | Characteristics |
| --- | --- |
| Operating Temperature Range(℃) | -55~+105 |
| Rated Voltage Range(V) | 6.3~100 |
| Capacitance Range(μF) | 0.47~15000 |
| Capacitance Tolerance(20℃,120Hz) | ±20% |
| Leakage current(μA) | 0.02CV or 3 whichever is greater (at 20℃,after 2 minutes) C:Nominal Capacitance (μF) V:Rated Voltage(V) |
| Dissipation Factor(20℃,120Hz) | Rated Voltage(V) 6.3 10 16 25 35 50 63 100 tanδ 0.22 0.19 0.16 0.14 0.12 0.10 0.09 0.08 when nominal capacitance is over 1000uF tanδ shall be added 0.02 to the listed value with increase of every 1000 uF |
| Characterislics of Low Temperature | Impedance at +10℃ 100KHz<200% of initial specified value at +20℃ ,100KHz(Impedance ratio at 100KHz) |
| Load Life(105℃) | After life test at condition stated in the tble below, the capacitors shall meet the following requirement. Case Dia Test time(hrs) ΦD≤8 1000 ΦD>8 2000 Ripple current applied Leakage Current Not more than the specified value. Capacitance Change within ±20% of the initial value. Dissipation Factor Not more than 200% of the specified value. |
| Shelf Life(105℃) | 1000hours. No voltage appiled. After test:UR to be applied for 30 minutes,24 to 48 hours before measurement. |

| DIMENSIONS mm | MULTIPLIER FOR RIPPLE CURRENT |
| --- | --- |

| ΦD 5 6.3 8 10 12.5 16 18 F 2.0 2.5 3.5 5.0 7.5 Φd 0.5 0.6 0.8 a 1.0 2.0 | Frequency coefficient Freq(Hz) Cap(μF) 120 1K 10K 100K 0.47~4.7 0.40 0.68 0.78 1.0 5.6~47 0.50 0.76 0.87 1.0 56~270 0.70 0.85 0.90 1.0 330~1000 0.80 0.93 0.98 1.0 1200~15000 0.90 0.95 1.0 1.0 Temperature coefficient Temperature(℃) +70 +85 +105 Factor 1.96 1.68 1.0 |
| --- | --- |

- STANDARD RATINGS

|  | WV(V) | 6.3 | 10 |
| --- | --- | --- | --- |
|  |  | Cap | Impedance(Ω)/100KHz | Ripple | Cap | Impedance(Ω)/100KHz | Ripple |
| ΦDxL(mm) |  |  |  |  |  |  |  |
|  |  | (μF) | 20℃ | -10℃ | mArms | (μF) | 20℃ | -10℃ | mArms |
| 5x11.5 | 100 | 0.65 | 1.3 | 175 | 82 | 1.65 | 1.3 | 175 |
| 5x15 | 150 | 0.46 | 0.92 | 235 | 100 | 0.46 | 0.92 | 235 |
| 6.3x11.5 | 220 | 0.30 | 0.60 | 290 | 180 | 0.31 | 0.62 | 290 |
| 6.3x15 | 330 | 0.20 | 0.40 | 400 | 220 | 0.20 | 0.40 | 400 |
| 8x12 | 470 | 0.17 | 0.34 | 488 | 330 | 0.17 | 0.34 | 490 |
| 8x15 | 680 | 0.13 | 0.26 | 617 | 470 | 0.13 | 0.26 | 617 |
| 8x20 | 1000 | 0.095 | 0.19 | 800 | 680 | 0.095 | 0.19 | 800 |
| 10x12.5 | 680 | 0.12 | 0.24 | 613 | 470 | 0.12 | 0.24 | 620 |
| 10x16 | 820 | 0.095 | 0.19 | 734 | 560 | 0.095 | 0.19 | 734 |
| 10x20 | 1200 | 0.065 | 0.13 | 1010 | 1000 | 0.060 | 0.13 | 1010 |
| 10x25 | 1500 | .055 | 0.11 | 1190 | 1200 | 0.055 | 0.11 | 1190 |
| 10x30 | 2200 | 0.045 | 0.090 | 1440 | 1500 | 0.045 | 0.090 | 1440 |
| 12.5x15 | 1200 | 0.065 | 0.13 | 1010 | 1000 | 0.065 | 0.13 | 1010 |
| 12.5x20 | 2200 | 0.042 | 0.084 | 1400 | 1800 | 0.042 | 0.084 | 1400 |
| 12.5x25 | 2700 | 0.038 | 0.076 | 1690 | 2200 | 0.036 | 0.072 | 1690 |
| 12.5x30 | 3900 | 0.032 | 0.064 | 1950 | 2700 | 0.032 | 0.064 | 1950 |
| 12.5x35 | 4700 | 0.028 | 0.056 | 2220 | 3300 | 0.028 | 0.056 | 2220 |
| 12.5x40 | 5600 | 0.026 | 0.052 | 2390 | 3900 | 0.025 | 0.050 | 2390 |
| 16x15 | 2700 | 0.046 | 0.092 | 1310 | 1800 | 0.046 | 0.092 | 1310 |
| 16x20 | 4700 | 0.034 | 0.068 | 1660 | 3300 | 0.034 | 0.068 | 1660 |
| 16x25 | 5600 | 0.028 | 0.056 | 2070 | 3900 | 0.028 | 0.056 | 2070 |
| 16x31.5 | 6800 | 0.025 | 0.050 | 2350 | 5600 | 0.025 | 0.050 | 2350 |
| 16x35.5 | 8200 | 0.022 | 0.044 | 2550 | 6800 | 0.022 | 0.044 | 2550 |
| 16x40 | 12000 | 0.020 | 0.040 | 2970 | 8200 | 0.020 | 0.040 | 2970 |
| 18x15 | 3300 | 0.043 | 0.086 | 1460 | 2200 | 0.043 | 0.086 | 1460 |
| 18x20 | 5600 | 0.030 | 0.060 | 1850 | 3900 | 0.030 | 0.060 | 1850 |
| 18x25 | 6800 | 0.027 | 0.054 | 2120 | 4700 | 0.027 | 0.054 | 2120 |
| 18x31.5 | 10000 | 0.023 | 0.046 | 2410 | 6800 | 0.023 | 0.046 | 2410 |
| 18x35.5 | 12000 | 0.019 | 0.038 | 2680 | 8200 | 0.019 | 0.038 | 2680 |
| 18x40 | 15000 | 0.018 | 0.036 | 3010 | 10000 | 0.018 | 0.036 | 3010 |

|  | WV(V) | 16 | 25 |
| --- | --- | --- | --- |
|  |  | Cap | Impedance(Ω)/100KHz | Ripple | Cap | Impedance(Ω)/100KHz | Ripple |
| ΦDxL(mm) |  |  |  |  |  |  |  |
|  |  | (μF) | 20℃ | -10℃ | mArms | (μF) | 20℃ | -10℃ | mArms |
| 5x11.5 | 56 | 0.65 | 1.3 | 175 | 39 | 0.65 | 1.3 | 175 |
| 5x15 | 82 | 0.46 | 0.92 | 235 | 56 | 0.46 | 0.92 | 235 |
| 6.3x11.5 | 120 | 0.31 | 0.62 | 290 | 82 | 0.31 | 0.62 | 290 |
| 6.3x15 | 180 | 0.20 | 0.40 | 400 | 120 | 0.20 | 0.40 | 400 |
| 8x12 | 270 | 0.17 | 0.34 | 501 | 180 | 0.17 | 0.34 | 503 |
| 8x15 | 330 | 0.13 | 0.26 | 575 | 220 | 0.13 | 0.26 | 575 |
| 8x20 | 470 | 0.095 | 0.19 | 760 | 330 | 0.095 | 0.19 | 751 |
| 10x12.5 | 330 | 0.13 | 0.26 | 625 | 220 | 0.12 | 0.24 | 629 |
| 10x16 | 390 | 0.090 | 0.18 | 795 | 270 | 0.090 | 0.18 | 795 |
| 10x20 | 680 | 0.065 | 0.13 | 1010 | 470 | 0.065 | 0.13 | 1010 |
| 10x25 | 820 | 0.055 | 0.11 | 1190 | 560 | 0.055 | 0.11 | 1190 |
| 10x30 | 1200 | 0.047 | 0.094 | 1430 | 820 | 0.045 | 0.090 | 1440 |
| 12.5x15 | 680 | 0.065 | 0.13 | 1010 | 470 | 0.065 | 0.13 | 1010 |
| 12.5x20 | 1200 | 0.042 | 0.084 | 1400 | 820 | 0.042 | 0.084 | 1400 |
| 12.5x25 | 1500 | 0.038 | 0.076 | 1690 | 1000 | 0.036 | 0.072 | 1690 |
| 12.5x30 | 2200 | 0.032 | 0.064 | 1950 | 1500 | 0.030 | 0.060 | 1950 |
| 12.5x35 | 2700 | 0.028 | 0.056 | 2200 | 1800 | 0.028 | 0.056 | 2200 |
| 12.5x40 | 3300 | 0.026 | 0.052 | 2390 | 2200 | 0.024 | 0.048 | 2390 |
| 16x15 | 1500 | 0.046 | 0.092 | 1340 | 820 | 0.046 | 0.092 | 1360 |
| 16x20 | 2200 | 0.034 | 0.068 | 1730 | 1500 | 0.034 | 0.068 | 1730 |
| 16x25 | 2700 | 0.028 | 0.056 | 2070 | 1800 | 0.028 | 0.056 | 2070 |
| 16x31.5 | 3900 | 0.025 | 0.050 | 2350 | 2700 | 0.025 | 0.050 | 2350 |
| 16x35.5 | 4700 | 0.022 | 0.044 | 2550 | 3300 | 0.022 | 0.044 | 2550 |
| 16x40 | 5600 | 0.020 | 0.040 | 2900 | 3900 | 0.020 | 0.040 | 2900 |
| 18x15 | 1500 | 0.043 | 0.086 | 1490 | 1200 | 0.043 | 0.086 | 1500 |
| 18x20 | 2700 | 0.030 | 0.060 | 1870 | 1800 | 0.036 | 0.072 | 1890 |
| 18x25 | 3900 | 0.027 | 0.054 | 2160 | 2700 | 0.027 | 0.054 | 2180 |
| 18x31.5 | 4700 | 0.023 | 0.046 | 2450 | 3300 | 0.023 | 0.046 | 2470 |
| 18x35.5 | 6800 | 0.019 | 0.038 | 2730 | 3900 | 0.019 | 0.038 | 2740 |
| 18x40 | 8200 | 0.018 | 0.036 | 3060 | 4700 | 0.018 | 0.036 | 3070 |

|  | WV(V) | 35 | 50 |
| --- | --- | --- | --- |
|  |  | Cap | Impedance(Ω)/100KHz | Ripple | Cap | Impedance(Ω)/100KHz | Ripple |
| ΦDxL(mm) |  |  |  |  |  |  |  |
|  |  | (μF) | 20℃ | -10℃ | mArms | (μF) | 20℃ | -10℃ | mArms |
| 5x11.5 | - | - | - | - | 0.47 | 3.9 | 7.8 | 22 |
| 5x11.5 | - | - | - | - | 1 | 3.5 | 7.0 | 36 |
| 5x11.5 | - | - | - | - | 2.2 | 3.0 | 6.0 | 54 |
| 5x11.5 | - | - | - | - | 3.3 | 2.6 | 5.2 | 63 |
| 5x11.5 | - | - | - | - | 4.7 | 2.2 | 4.4 | 75 |
| 5x11.5 | - | - | - | - | 10 | 1.4 | 2.8 | 110 |
| 5x11.5 | 27 | 0.65 | 1.3 | 175 | 18 | 0.95 | 1.9 | 120 |
| 5x15 | 39 | 0.46 | 0.92 | 235 | 27 | 0.55 | 1.1 | 135 |
| 6.3x11.5 | 56 | 0.30 | 0.060 | 290 | 39 | 0.36 | 0.72 | 148 |
| 6.3x15 | 82 | 0.20 | 0.040 | 400 | 56 | 0.28 | 0.56 | 153 |
| 8x12 | 120 | 0.17 | 0.034 | 506 | 68 | 0.20 | 040 | 360 |
| 8x15 | 180 | 0.13 | 0.026 | 637 | 82 | 0.18 | 0.36 | 460 |
| 8x20 | 220 | 0.095 | 0.019 | 760 | 120 | 0.13 | 0.26 | 670 |
| 10x12.5 | 150 | 0.12 | 0.024 | 635 | 82 | 0.18 | 0.36 | 443 |
| 10x16 | 180 | 0.095 | .019 | 795 | 100 | 0.15 | 0.30 | 553 |
| 10x20 | 330 | 0.065 | 0.013 | 1010 | 180 | 0.085 | 0.17 | 676 |
| 10x25 | 390 | 0.055 | 0.011 | 1190 | 220 | 0.075 | 0.15 | 876 |
| 10x30 | 560 | 0.045 | 0.090 | 1450 | 330 | 0.055 | 0.11 | 1010 |
| 12.5x15 | 330 | 0.065 | 0.013 | 1010 | 180 | 0.095 | 0.19 | 745 |
| 12.5x20 | 560 | 0.042 | 0.084 | 1400 | 330 | 0.060 | 0.12 | 979 |
| 12.5x25 | 680 | 0.038 | 0.076 | 1690 | 470 | 0.044 | 0.088 | 1180 |
| 12.5x30 | 1000 | 0.032 | 0.064 | 1950 | 560 | 0.040 | 0.080 | 1310 |
| 12.5x35 | 1200 | 0.028 | 0.056 | 2200 | 680 | 0.036 | 0.072 | 1470 |
| 12.5x40 | 1500 | 0.026 | 0.052 | 2390 | 820 | 0.034 | 0.068 | 1590 |
| 16x15 | 560 | 0.046 | 0.092 | 1360 | 330 | 0.065 | 0.13 | 982 |
| 16x20 | 1000 | 0.034 | 0.068 | 1730 | 680 | 0.045 | 0.090 | 1210 |
| 16x25 | 1200 | 0.028 | 0.056 | 2070 | 820 | 0.038 | 0.076 | 1490 |
| 16x31.5 | 1800 | 0.025 | 0.050 | 2350 | 1000 | 0.032 | 0.064 | 1890 |
| 16x35.5 | 2200 | 0.022 | 0.044 | 2550 | 1200 | 0.028 | 0.056 | 2140 |
| 16x40 | 2700 | 0.020 | 0.040 | 2900 | 1500 | 0.026 | 0.052 | 2410 |
| 18x15 | 680 | 0.043 | 0.086 | 1520 | 470 | 0.048 | 0.096 | 1080 |
| 18x20 | 1200 | 0.036 | 0.072 | 1900 | 820 | 0.036 | 0.072 | 1450 |
| 18x25 | 1800 | 0.027 | 0.054 | 2200 | 1000 | 0.032 | 0.064 | 1720 |
| 18x31.5 | 2200 | 0.023 | 0.046 | 2490 | 1500 | 0.026 | 0.052 | 1970 |
| 18x35.5 | 2700 | 0.019 | 0.038 | 2770 | 1800 | 0.025 | 0.050 | 2310 |
| 18x40 | 3300 | 0.018 | 0.036 | 3110 | 2200 | 0.024 | 0.048 | 2530 |

|  | WV(V) |  |  |
| --- | --- | --- | --- |
|  |  | Cap | Impedance(Ω)/100KHz | Ripple | Cap | Impedance(Ω)/100KHz | Ripple |
| ΦDxL(mm) |  |  |  |  |  |  |  |
|  |  | (μF) | 20℃ | -10℃ | mArms | (μF) | 20℃ | -10℃ | mArms |
| 5x11.5 | 12 | 1.2 | 3.6 | 120 | 5.6 | 1.9 | 7.6 | 57 |
| 5x15 | 18 | 0.85 | 2.6 | 135 | 8.2 | 1.3 | 5.2 | 74 |
| 6.3x11.5 | 27 | 0.55 | 1.7 | 148 | 12 | 1.1 | 4.4 | 78 |
| 6.3x15 | 39 | 0.38 | 1.1 | 153 | 18 | 0.62 | 2.5 | 85 |
| 8x12 | 47 | 0.32 | 0.96 | 360 | 22 | 0.53 | 2.1 | 275 |
| 8x15 | 68 | 0.24 | 0.72 | 469 | 33 | 0.35 | 1.4 | 360 |
| 8x20 | 82 | 0.17 | 0.51 | 682 | 39 | 0.27 | 1.1 | 490 |
| 10x12.5 | 56 | 0.23 | 0.69 | 448 | 27 | 0.47 | 1.9 | 319 |
| 10x16 | 68 | 0.17 | 0.51 | 553 | 33 | 0.32 | 1.3 | 424 |
| 10x20 | 120 | 0.12 | 0.36 | 676 | 56 | 0.25 | 1.0 | 499 |
| 10x25 | 150 | 0.10 | 0.30 | 876 | 68 | 0.18 | 0.72 | 634 |
| 10x30 | 180 | 0.085 | 0.26 | 1020 | 100 | 0.15 | 0.60 | 739 |
| 12.5x15 | 150 | 0.11 | 0.33 | 745 | 68 | 0.20 | 0.80 | 613 |
| 12.5x25 | 220 | 0.075 | 0.23 | 979 | 100 | 0.13 | 0.52 | 805 |
| 12.5x25 | 270 | 0.065 | 0.20 | 1180 | 120 | 0.11 | 0.44 | 857 |
| 12.5x30 | 390 | 0.055 | 0.17 | 1310 | 180 | 0.090 | 0.36 | 1120 |
| 12.5x35 | 470 | 0.048 | 0.14 | 1470 | 220 | 0.075 | 0.30 | 1240 |
| 12.5x40 | 560 | 0.042 | 0.13 | 1590 | 270 | 0.060 | 0.24 | 1330 |
| 16x15 | 220 | 0.080 | 0.24 | 982 | 120 | 0.13 | 0.52 | 706 |
| 16x20 | 390 | 0.057 | 0.17 | 1210 | 180 | 0.11 | 0.44 | 916 |
| 16x25 | 470 | 0.052 | 0.16 | 1490 | 220 | 0.081 | 0.32 | 1290 |
| 16x31.5 | 680 | 0.042 | 0.13 | 1890 | 330 | 0.059 | 0.23 | 1630 |
| 16x35.5 | 820 | 0.036 | 0.11 | 2140 | 390 | 0.052 | 0.21 | 1750 |
| 16x40 | 1000 | 0.032 | 0.096 | 2410 | 470 | 0.045 | 0.18 | 1920 |
| 18x15 | 330 | 0.065 | 0.20 | 1200 | 150 | 0.12 | 0.48 | 871 |
| 18x20 | 470 | 0.058 | 0.17 | 1460 | 270 | 0.085 | 0.34 | 1170 |
| 18x25 | 680 | 0.050 | 0.15 | 1740 | 330 | 0.071 | 0.28 | 1500 |
| 18x31.5 | 820 | 0.042 | 0.13 | 1990 | 390 | 0.058 | 0.23 | 1630 |
| 18x35.5 | 1000 | 0.035 | 0.11 | 2340 | 560 | 0.054 | 0.22 | 1920 |
| 18x40 | 1200 | 0.032 | 0.096 | 2560 | 680 | 0.041 | 0.16 | 2100 |

Ripple Current: 105℃,100KHz