| ACDC_LinkSwitch-XT_102706; Rev.1.18; Copyright Power Integrations 2006 | INPUT | INFO | OUTPUT | UNIT | ACDC_LinkSwitch-XT_102706_Rev1-18.xls; LinkSwitch-XT Continuous/Discontinuous Flyback Transformer Design Spreadsheet |
| --- | --- | --- | --- | --- | --- |
| ENTER APPLICATION VARIABLES |  |  |  |  | Customer |
| VACMIN | 190 |  |  | Volts | Minimum AC Input Voltage |
| VACMAX | 265 |  |  | Volts | Maximum AC Input Voltage |
| fL | 50 |  |  | Hertz | AC Mains Frequency |
| VO | 12.00 |  |  | Volts | Output Voltage (main) (For CC designs enter upper CV tolerance limit) |
| IO | 0.40 |  |  | Amps | Power Supply Output Current (For CC designs enter upper CC tolerance limit) |
| CC Threshold Voltage | 0.00 |  |  | Volts | Voltage drop across sense resistor. |
| Output Cable Resistance |  |  | 0.17 | Ohms | Enter the resistance of the output cable (if used) |
| PO |  |  | 4.83 | Watts | Output Power (VO x IO + CC dissipation) |
| Feedback Type | Opto |  | Opto |  | Choose 'BIAS' for Bias winding feedback and 'OPTO' for Optocoupler feedback from the 'Feedback Type' drop down box at the top of this spreadsheet |
| Add Bias Winding | No |  | No |  | Choose 'YES' in the 'Bias Winding' drop down box at the top of this spreadsheet to add a Bias winding. Choose 'NO' to continue design without a Bias winding. Addition of Bias winding can lower no load consumption |
| Clampless design (LNK 362 only) | No |  | External Clamp |  | Choose 'YES' from the 'clampless Design' drop down box at the top of this spreadsheet for a clampless design. Choose 'NO' to add an external clamp circuit. Clampless design lowers the total cost of the power supply |
| n |  |  | 0.7 |  | Efficiency Estimate at output terminals. |
| Z | 0.50 |  | 0.5 |  | Loss Allocation Factor (suggest 0.5 for CC=0 V, 0.75 for CC=1 V) |
| tC | 2.90 |  |  | mSeconds | Bridge Rectifier Conduction Time Estimate |
| CIN | 5.50 |  |  | uFarads | Input Capacitance |
| Input Rectification Type | F |  | F |  | Choose H for Half Wave Rectifier and F for Full Wave Rectification from the 'Rectification' drop down box at the top of this spreadsheet |
| ENTER LinkSwitch-XT VARIABLES |  |  |  |  |  |
| LinkSwitch-XT | Auto |  | LNK364 |  | Recommended LinkSwitch-XT device |
| Chosen Device |  | LNK364 |  |  |  |
| ILIMITMIN |  |  | 0.233 | Amps | Minimum Current Limit |
| ILIMITMAX |  |  | 0.268 | Amps | Maximum Current Limit |
| fSmin |  |  | 124000 | Hertz | Minimum Device Switching Frequency |
| I^2fmin |  |  | 7425 | A^2Hz | I^2f (product of current limit squared and frequency is trimmed for tighter tolerance) |
| VOR | 90.00 |  | 90 | Volts | Reflected Output Voltage |
| VDS |  |  | 10 | Volts | LinkSwitch-XT on-state Drain to Source Voltage |
| VD |  |  | 0.7 | Volts | Output Winding Diode Forward Voltage Drop |
| KP |  |  | 1.39 |  | Ripple to Peak Current Ratio (0.6 < KP < 6.0). For Clampless Designs use KP > 1.1 |
| ENTER TRANSFORMER CORE/CONSTRUCTION VARIABLES |  |  |  |  |  |
| Core Type | EE13 |  | EE13 |  | User-Selected transformer core |
| Core |  | EE13 |  | P/N: | PC40EE13-Z |
| Bobbin |  | EE13_BOBBIN |  | P/N: | EE13_BOBBIN |
| AE |  |  | 0.171 | cm^2 | Core Effective Cross Sectional Area |
| LE |  |  | 3.02 | cm | Core Effective Path Length |
| AL |  |  | 1130 | nH/T^2 | Ungapped Core Effective Inductance |
| BW |  |  | 7.9 | mm | Bobbin Physical Winding Width |
| M |  |  | 0 | mm | Safety Margin Width (Half the Primary to Secondary Creepage Distance) |
| L | 3.00 |  | 3 |  | Number of Primary Layers |
| NS | 22 |  | 22 |  | Number of Secondary Turns |
| NB |  |  | N/A |  | Bias winding not used |
| VB |  |  | N/A | Volts | Bias winding not used |
| PIVB |  |  | N/A | Volts | N/A - Bias Winding not in use |
| DC INPUT VOLTAGE PARAMETERS |  |  |  |  |  |
| VMIN |  |  | 233 | Volts | Minimum DC Input Voltage |
| VMAX |  |  | 375 | Volts | Maximum DC Input Voltage |
| CURRENT WAVEFORM SHAPE PARAMETERS |  |  |  |  |  |
| DMAX |  |  | 0.22 |  | Maximum Duty Cycle |
| IAVG |  |  | 0.03 | Amps | Average Primary Current |
| IP |  |  | 0.23 | Amps | Minimum Peak Primary Current |
| IR |  |  | 0.23 | Amps | Primary Ripple Current |
| IRMS |  |  | 0.07 | Amps | Primary RMS Current |
| TRANSFORMER PRIMARY DESIGN PARAMETERS |  |  |  |  |  |
| LP |  |  | 1737 | uHenries | Typical Primary Inductance. +/- 10% |
| LP_TOLERANCE |  |  | 10 | % | Primary inductance tolerance |
| NP |  |  | 156 |  | Primary Winding Number of Turns |
| ALG |  |  | 71 | nH/T^2 | Gapped Core Effective Inductance |
| BM |  | Info | 1746 | Gauss | !!! Info. Flux densities above ~ 1500 Gauss may produce audible noise. Verify with dip varnished sample transformers. Increase NS to greater than or equal to 27 turns or increase VOR |
| BAC |  |  | 873 | Gauss | AC Flux Density for Core Loss Curves (0.5 X Peak to Peak) |
| ur |  |  | 1588 |  | Relative Permeability of Ungapped Core |
| LG |  |  | 0.28 | mm | Gap Length (Lg > 0.1 mm) |
| BWE |  |  | 23.7 | mm | Effective Bobbin Width |
| OD |  |  | 0.15 | mm | Maximum Primary Wire Diameter including insulation |
| INS |  |  | 0.03 | mm | Estimated Total Insulation Thickness (= 2 * film thickness) |
| DIA |  |  | 0.12 | mm | Bare conductor diameter |
| AWG |  |  | 37 | AWG | Primary Wire Gauge (Rounded to next smaller standard AWG value) |
| CM |  |  | 20 | Cmils | Bare conductor effective area in circular mils |
| CMA |  |  | 297 | Cmils/Amp | Primary Winding Current Capacity (150 < CMA < 500) |
| TRANSFORMER SECONDARY DESIGN PARAMETERS |  |  |  |  |  |
| Lumped parameters |  |  |  |  |  |
| ISP |  |  | 1.65 | Amps | Peak Secondary Current |
| ISRMS |  |  | 0.76 | Amps | Secondary RMS Current |
| IRIPPLE |  |  | 0.64 | Amps | Output Capacitor RMS Ripple Current |
| CMS |  |  | 151 | Cmils | Secondary Bare Conductor minimum circular mils |
| AWGS |  |  | 28 | AWG | Secondary Wire Gauge (Rounded up to next larger standard AWG value) |
| DIAS |  |  | 0.32 | mm | Secondary Minimum Bare Conductor Diameter |
| ODS |  |  | 0.36 | mm | Secondary Maximum Outside Diameter for Triple Insulated Wire |
| INSS |  |  | 0.02 | mm | Maximum Secondary Insulation Wall Thickness |
| VOLTAGE STRESS PARAMETERS |  |  |  |  |  |
| VDRAIN |  |  | 584 | Volts | Maximum Drain Voltage Estimate (Includes Effect of Leakage Inductance) |
| PIVS |  |  | 65 | Volts | Output Rectifier Maximum Peak Inverse Voltage |
| FEEDBACK COMPONENTS |  |  |  |  |  |
| Recommended Bias Diode |  |  | 1N4003 - 1N4007 |  | Recommended diode is 1N4003. Place diode on return leg of bias winding for optimal EMI. See LinkSwitch-XT Design Guide |
| R1 |  |  | 500 - 1000 | ohms | CV bias resistor for CV/CC circuit. See LinkSwitch-XT Design Guide |
| R2 |  |  | 200 - 820 | ohms | Resistor to set CC linearity for CV/CC circuit. See LinkSwitch-XT Design Guide |
| TRANSFORMER SECONDARY DESIGN PARAMETERS (MULTIPLE OUTPUTS) |  |  |  |  |  |
| 1st output |  |  |  |  |  |
| VO1 |  |  | 12.00 | Volts | Main Output Voltage (if unused, defaults to single output design) |
| IO1 |  |  | 0.40 | Amps | Output DC Current |
| PO1 |  |  | 4.83 | Watts | Output Power |
| VD1 |  |  | 0.70 | Volts | Output Diode Forward Voltage Drop |
| NS1 |  |  | 22.00 |  | Output Winding Number of Turns |
| ISRMS1 |  |  | 0.76 | Amps | Output Winding RMS Current |
| IRIPPLE1 |  |  | 0.65 | Amps | Output Capacitor RMS Ripple Current |
| PIVS1 |  |  | 64.88 | Volts | Output Rectifier Maximum Peak Inverse Voltage |
| Recommended Diodes |  |  | SB180 |  | Recommended Diodes for this output |
| Pre-Load Resistor |  |  | 4 | k-Ohms | Recommended value of pre-load resistor |
| CMS1 |  |  | 152.10 | Cmils | Output Winding Bare Conductor minimum circular mils |
| AWGS1 |  |  | 28.00 | AWG | Wire Gauge (Rounded up to next larger standard AWG value) |
| DIAS1 |  |  | 0.32 | mm | Minimum Bare Conductor Diameter |
| ODS1 |  |  | 0.36 | mm | Maximum Outside Diameter for Triple Insulated Wire |
| 2nd output |  |  |  |  |  |
| VO2 |  |  |  | Volts | Output Voltage |
| IO2 |  |  |  | Amps | Output DC Current |
| PO2 |  |  | 0.00 | Watts | Output Power |
| VD2 |  |  | 0.70 | Volts | Output Diode Forward Voltage Drop |
| NS2 |  |  | 1.21 |  | Output Winding Number of Turns |
| ISRMS2 |  |  | 0.00 | Amps | Output Winding RMS Current |
| IRIPPLE2 |  |  | 0.00 | Amps | Output Capacitor RMS Ripple Current |
| PIVS2 |  |  | 2.91 | Volts | Output Rectifier Maximum Peak Inverse Voltage |
| Recommended Diode |  |  |  |  | Recommended Diodes for this output |
| CMS2 |  |  | 0.00 | Cmils | Output Winding Bare Conductor minimum circular mils |
| AWGS2 |  |  | N/A | AWG | Wire Gauge (Rounded up to next larger standard AWG value) |
| DIAS2 |  |  | N/A | mm | Minimum Bare Conductor Diameter |
| ODS2 |  |  | N/A | mm | Maximum Outside Diameter for Triple Insulated Wire |
| 3rd output |  |  |  |  |  |
| VO3 |  |  |  | Volts | Output Voltage |
| IO3 |  |  |  | Amps | Output DC Current |
| PO3 |  |  | 0.00 | Watts | Output Power |
| VD3 |  |  | 0.70 | Volts | Output Diode Forward Voltage Drop |
| NS3 |  |  | 1.21 |  | Output Winding Number of Turns |
| ISRMS3 |  |  | 0.00 | Amps | Output Winding RMS Current |
| IRIPPLE3 |  |  | 0.00 | Amps | Output Capacitor RMS Ripple Current |
| PIVS3 |  |  | 2.91 | Volts | Output Rectifier Maximum Peak Inverse Voltage |
| Recommended Diode |  |  |  |  | Recommended Diodes for this output |
| CMS3 |  |  | 0.00 | Cmils | Output Winding Bare Conductor minimum circular mils |
| AWGS3 |  |  | N/A | AWG | Wire Gauge (Rounded up to next larger standard AWG value) |
| DIAS3 |  |  | N/A | mm | Minimum Bare Conductor Diameter |
| ODS3 |  |  | N/A | mm | Maximum Outside Diameter for Triple Insulated Wire |
| Total power |  |  | 4.83 | Watts | Total Output Power |
| Negative Output |  |  | N/A |  | If negative output exists enter Output number; eg: If VO2 is negative output, enter 2 |