# Universal, Off-Line, High Brightness, 350mA LED Driver

## SUMMARY AND FEATURES

- Wide Input Voltage - 85 to 265VAC, 50/60Hz

- Constant Current Regulation for Uniform Illumination

- Output Current Adjustable

## DEMO BOARD GENERAL DESCRIPTION

The FT871DB1 demo board is a High-Brightness LED power driver to supply a string of LEDs using the FT871 IC from a universal AC input voltage. The FT871DB1 can supply a maximum output current of 350mA to drive 9V LED strings from a wide input voltage - 85 to 265VAC, 50/60Hz.

The report contains the LED driver specification, a circuit diagram, a complete bill of materials, the printed circuit board layouts, and performance data.

Figure 1.  Demo Board Picture

## System Specification

| DESCRIPTION | SYMBOL | MIN | TYP | MAX | UNITS | COMMENT |
| --- | --- | --- | --- | --- | --- | --- |
| Input |
| Voltage | Vin | 85 |  | 265 | VAC |  |
| Frequency | Fline |  | 50 |  | Hz |  |
| Output |
| Output voltage | Vout | 8 | 8.6 | 9 | V |  |
| Output current | Iout | 330 | 350 | 370 | mA |  |
| Efficiency |
| Full Load |  | 73 | 76 | 80 | % | VLD>750mV |
| Switching frequency |
| Oscillator frequency | Fosc | 20 | 25 | 30 | KHz | FT871A |
| Oscillator Modulation Swing | ∆ Fosc |  | ±4 |  | % |  |

## SCHEMATIC

Figure 2.  Demo Board Schematic

## PCB LAYOUT

Top View

Bottom View

Figure 3.  Printed Circuit Layout

## BILL OF MATERIALS

| RefDes | DESCRIPTION | QTY | PACKAGE | MANUFA CTURE | MANUFACTURE’S PART NUMBER |
| --- | --- | --- | --- | --- | --- |
| B1 | 400V, 1A single phase diode bridge | 1 | DBS | STS | DB104S |
| C1 | 0.047μF, 300VAC EMI suppression capacitor | 1 | Radial |  |  |
| C2，C3 | 10μF, 400V electrolytic capacitor | 1 | Radial |  |  |
| C4，C5，C8 | 1nF, 25V ceramic chip capacitor | 3 | SMD0805 |  |  |
| C6 | 100pF ceramic chip capacitor | 1 | SMD0805 |  |  |
| C7 | 4.7μF,25V electrolytic capacitor | 1 | Radial |  |  |
| C9 | 0.47μF, 400V metal film capacitor | 1 | Radial |  |  |
| D1，D2，D3 | 1000V, 1A diode | 1 | SMB |  | 1N4007 |
| D4 | 600V, 1A ultrafast diode | 1 | SMB | ON Semi | MURS160T3 |
| D5 | 600V, 1A ultrafast diode | 1 | SMB | ON Semi | MURS160T3 |
| D6 | 12V，0.5WZener diode | 1 | Axial |  |  |
| F1 | 2A ,250VAC fuse | 1 | Axial |  |  |
| J1,J2 | 2 position, 0.156” pitch, vertical header | 2 |  |  |  |
| L1 | 2.2mH, 400mA rms, 600mA sat inductor | 1 | Radial |  |  |
| L2 | 20uH, 200mA rms, 600mA sat inductor | 1 | Radial |  |  |
| Q1 | 600V,4A, N-channel FET | 1 | DPAK |  | 4N60 |
| RT1 | 50Ω NTC inrush limiter | 1 | Radial |  |  |
| R2 | 5KΩ top adjust trimpot | 1 | SMT |  |  |
| R4 | 0Ω chip resistor | 1 | SMD0805 |  |  |
| R5 | 22KΩ, 1/2Wchip resistor | 1 | SMD1812 |  |  |
| R6 | 1.8Ω, 1/8Wchip resistor | 1 | SMD0805 |  |  |
| R7 | 1.2Ω, 1/8Wchip resistor | 1 | SMD0805 |  |  |
| R8 | 0Ω chip resistor | 1 | SMD0805 |  |  |
| R9 | 100Ω top adjust trimpot | 1 | SMT |  |  |
| R10 | 0Ω chip resistor | 1 | SMD0805 |  |  |
| U1 | Universal LED Driver | 1 | SOP8 | FMD | FT871 |

## PERFORMANCE DATA

### Efficiency

Figure 4  Efficiency vs. Vin

### Line Regulation

Figure 5  Line Regulation