#### Panther 100W

#### AFB Converter Test Simple Report

#### (320Vdc~420Vdc, 12V Output, 0~7A Load)

Test conditions

If it is not specified express, the Nominal Testing Conditions suppose:

-Ambient Temperature: 25℃

List of the main test equipment

| Item | Test equipment | Main Features | Recommended |
| --- | --- | --- | --- |
| 1 | High voltage DC Source | Adjustable, 0 to 300Vac, 50Hz, 1000W | Chroma 61602 |
| 2 | Low voltage DC Source | Adjustable, 0 to 30Vdc | Topward 6306D |
| 3 | Electronic Load | 16V/100W | Chroma 63010 |
| 4 | Multimeter |  | Fluke 189 |
| 5 | Oscilloscope | 4 channel, 300MHz 4 channel, 350MHz | Tektronix, TDS 3034B |

# 0. Summary

## 0.1 Results Summary

| Test Item | Specification | Test Result |
| --- | --- | --- |
| 1. VCC Turn-on and Turn-off Thresholds |
| Turn-on Threshold | 12V | 11.65V |
| Turn-off Threshold | 10V | 10.17V |
| 2. VBO Turn-on and Turn-off Thresholds (1V/15uA hysteresis) |
| Turn-on Threshold |  | 372Vdc |
| Turn-off Threshold |  | 317Vdc |
| 3. Efficiency Vs Vin |
| Vin=420Vdc | Vcc=15V 7A Load | 88.9% |
| Vin=380Vdc |  | 89.6% |
| Vin=320Vdc |  | 89.2% |
| 4. Dynamic response Peak to Peak value |
| Vin=420Vac | 30% Imax to 80% Imax | <±0.15 |
| Vin=380Vac |  | <±0.15 |
| Vin=320Vac |  | <±0.15 |
| 5. Operation frequency (0~100W) |
| Vin=420Vdc | Rton=24K Rtoff=30K | 101KHz~105KHz |
| Vin=380Vdc |  | 97KHz~101KHz |
| Vin=320Vdc |  | 89KHz~94KHz |
| 6. Cycle by cycle OCP Function |
| In soft start up | All condition | OK |
| Works well then output short circuit | All condition | Ok |
| 7. OVP Function |
| Feedback loop open | All condition | Ok |
| 8. OTP Function |
| Votp below 1/8.5Vcc | All condition | Ok |

## 0.2 Schematic

Demo board circuit

Red components means the parts have not welded in this application circuit.

Green components means the parts have been added in this application circuit.

Simple test circuit

## 0.3 Test Data

Load Regulation

Efficiency

## 0.4 Key Waveform

Primary side MOSFET ZVS:

Test condition: Vin=380V, Vcc=15V, Iload=7A

Ch1-LG, Ch2-HG, Ch3-Va, Ch4-Iintransformer

Test condition: Vin=380V, Vcc=15V, Iload=0A

Ch1-LG, Ch2-HG, Ch3-Va, Ch4-Iintransformer

Secondary side Diode ZCS:

Test condition: Vin=380V, Vcc=15V, Iload=7A

Ch1-LG, Ch2-HG, Ch3-Va, Ch4-Iin secondary side Diode

Test condition: Vin=380V, Vcc=15V, Iload=0A

Ch1-LG, Ch2-HG, Ch3-Va, Ch4-Iin secondary side Diode

# IMPORTANT NOTICE

No portion of O2Micro specifications/datasheets or any of its subparts may be reproduced in any form, or by any means, without prior written permission from O2Micro.

O2Micro and its subsidiaries reserve the right to make changes to their datasheets and/or products or to discontinue any product or service without notice, and advise customers to obtain the latest version of relevant information to verify, before placing orders, that information being relied on is current and complete. All products are sold subject to the terms and conditions of sale supplied at the time of order acknowledgment, including those pertaining to warranty, patent infringement, and limitation of liability.

O2Micro warrants performance of its products to the specifications applicable at the time of sale in accordance with O2Micro’s standard warranty. Testing and other quality control techniques are utilized to the extent O2Micro deems necessary to support this warranty. Specific testing of all parameters of each device is not necessarily performed, except those mandated by government requirements.

Customer acknowledges that O2Micro products are not designed, manufactured or intended for incorporation into any systems or products intended for use in connection with life support or other hazardous activities or environments in which the failure of the O2Micro products could lead to death, bodily injury, or property or environmental damage (“High Risk Activities”). O2Micro hereby disclaims all warranties, and O2Micro will have no liability to Customer or any third party, relating to the use of O2Micro products in connection with any High Risk Activities.

Any support, assistance, recommendation or information (collectively, “Support”) that O2Micro may provide to you (including, without limitation, regarding the design, development or debugging of your circuit board or other application) is provided “AS IS.” O2Micro does not make, and hereby disclaims, any warranties regarding any such Support, including, without limitation, any warranties of merchantability or fitness for a particular purpose, and any warranty that such Support will be accurate or error free or that your circuit board or other application will be operational or functional. O2Micro will have no liability to you under any legal theory in connection with your use of or reliance on such support.

Copyright © 2009, O2Micro International Limited