## Slide 1
Active Clamp Forward Reset Technique Using the UCC2891 PWM Controller
Steve Mappus

## Slide 2: Agenda
Traditional Transformer Reset Techniques
  Third Winding, RCD Clamp, Resonant Reset
Active Clamp Reset Forward Topology
  High Side Clamp
  Low Side Clamp
  Timing Diagrams
  ZVS Design Considerations
Introducing the UCC2891/2/3/4
  Features, Part Differences, Applications
UCC2891 EVM
  Active Clamp Operation and Performance Characteristics
  Transformer Design Considerations
  Primary and Secondary Gate Drives
  ZVS Waveforms
  Possible Performance Improvements
Reference Materials
UCC2891 Final Thoughts

## Slide 3: Traditional Transformer Reset Techniques
Advantages
  Low Complexity
  Low Voltage Stress
  Recycled Inductive Energy
Disadvantages
  Hard-switching
  50% Duty Cycle Limit
  Lower Transformer Turns Ratio
  Increased Transformer Leakage
Advantages
  >50% Duty Cycle
  Simple Transformer Design
Disadvantages
  Hard-switching
  Higher Voltage Stress
  Dissipative Inductive Energy
  Clamp R Losses
(A) Third Winding
(B) RCD Clamp
(C) Resonant Reset
Advantages
  Fewest Components
  Simple Transformer Design
  Recycled Inductive Energy
  Reduced EMI
  >50% Duty Cycle
Disadvantages
  Hard-switching
  Parasitic L and C Variation
  Higher Voltage Stress
  Self-Driven Synchronous Rectification not Intuitive

## Slide 4: Active Clamp Reset Technique
Applicable to Forward and Flyback Topologies
Active Clamp Applied to Either High Side or Low Side
Advantages
  Natural ZVS (Zero Voltage Switching) for Highest Efficiency
  Fixed Frequency Operation
  Higher Frequency Operation Possible
  >50% Duty Cycle
  Recycles Inductive Energy
  Reduced EMI
  Easy to Adapt Self-Driven Synchronous Rectification
Disadvantages
  Additional MOSFET Switch Required for Active Reset
  Gate Drive Circuitry somewhat Complex
  Precision Max Duty Cycle Clamp is Critical
  Advanced PWM Control Technique Required

## Slide 5: High-Side (Flyback) Active Clamp
Advantages
  Vcl Lower than Low-Side Clamp
  Q2 is N-Channel, More Selection
  Smaller Clamp Cap Value
Disadvantages
  Gate Drive Transformer for Q2

## Slide 6: Low-Side (Boost) Active Clamp
Advantages
  Direct Gate drive to Q2
  Precise Delay Timing for ZVS
  Same Vds as High-Side
Disadvantages
  Larger Clamp Cap Value
  Higher Clamp Voltage than High-Side
  Q2 is P-Channel, Less Selection

## Slide 7: Active Clamp Timing - Power Transfer
 | Q1 | Q2 | Q3 | Q4 | D1 | D2 | D3 | D4
t0t1 | ON | OFF | ON | OFF | OFF | OFF | OFF | OFF
SWITCH | ZVS |  | NON ZVS |  |  |  |  | 
t0t1 Dominant Losses
  Q1 - Conduction
  Q3 – Switching, Conduction

## Slide 8: Active Clamp Timing - Resonant
 | Q1 | Q2 | Q3 | Q4 | D1 | D2 | D3 | D4
t1t2 | OFF | OFF | OFF | OFF | OFF | ON | OFF | ON
SWITCH | ZVS |  | ZVS |  |  |  |  | 
t1t2 Dominant Losses
  Q2 – Body-Diode Conduction (Magnetizing Current Only)
  Q4 – Body-Diode Conduction

## Slide 9: Active Clamp Timing - Clamp
 | Q1 | Q2 | Q3 | Q4 | D1 | D2 | D3 | D4
t2t3 | OFF | ON | OFF | ON | OFF | OFF | OFF | OFF
SWITCH |  | ZVS |  | ZVS |  |  |  | 
t2t3 Dominant Losses
  Q2 – Conduction (Magnetizing Current Only)
  Q4 - Conduction

## Slide 10: Active Clamp Timing - Resonant
 | Q1 | Q2 | Q3 | Q4 | D1 | D2 | D3 | D4
t3t4 | OFF | OFF | OFF | OFF | ON | OFF | OFF | ON
SWITCH |  | ZVS |  | ZVS |  |  |  | 
t3t4 Dominant Losses
  Q4 – Body-Diode Conduction
  Q1 – Body-Diode Conduction (Magnetizing Current Only)
t4t0 Repeat

## Slide 11: Q1 Turn-On ZVS Conditions
1. Identify Main ZVS Parasitic Elements
2. Define Delay Time
3. Q1 Turn-On ZVS Requirements
Always Turn-On ZVS
as
then,
Light Load, High Vin
ZVS Not Always Possible
Always Turn-Off ZVS

## Slide 12: Q1 ZVS Simplified
Resonant Cycle at Q1 Turn-On
  ZVS Achieved if:
Resonant Cycle at Q1 Turn-Off
  Always Achieve ZVS
  Resonant Capacitance Naturally Discharges in Same Direction as Resonant Current
  Resonant Current dominated by IMAG
  IMAG is Peak at Q1 Turn-Off
  Within Set Delay Time

## Slide 13: Introducing the UCC2891/2/3/4
Not a UCC3580 Replacement
Current Mode Control
Cycle by Cycle Current Limit
Dedicated AUX Output
Programmable Delay
Precise Max Duty Cycle Clamp
Programmable Internal Slope Compensation
Synchronizable Oscillator
HV Internal Start-Up Device
Programmable Soft-Start
Programmable Line Monitor
TrueDrive 2A Sink Source Output

## Slide 14: UCC289/1/2/3/4 Part Differences
UCC289/1/2/3/4 Targeted Markets
  Merchant Power
  48-V Telecom Power Modules
  Datacom and General Computer
  42-V Automotive Systems
  Off-Line Power Converters
Active Clamp Forward
  Typically Limited to 600W
Active Clamp Flyback
  Typically Limited to 200W
Version | 110V Startup Circuit | Application | CS Threshold + Slope Comp
UCC2891 | Yes | 24-48V Input DC/DC Systems | 0.8V
UCC2892 | No | Off-line or Low Input Voltage Systems | 1.25V
UCC2893 | Yes | 24-48V Input DC/DC Systems | 0.8V
UCC2894 | No | Off-line or Low Input Voltage Systems | 1.25V

## Slide 15: UCC2891 EVM
EVM Features
  100W Half Brick
  Active Clamp Forward
  Self-Driven Synchronous Rectification
  ZVS High Efficiency
  Very Low Component Count
  Low Input Line Monitor
  Output Short Circuit Protection
  Regulates to Zero Load
Specifications
  36V < VIN < 75V
  0A < IOUT < 30A
  VO = 3.3V  1%
  FS = 300kHz
  Line Reg < 0.1%
  Load Reg < 0.1%

## Slide 16: UCC2891 EVM Schematic

## Slide 17: UCC2891 Transformer Waveforms
Active Clamp Transformer Characteristics
  Can Operate in Third Quadrant (Q3) of BH Curve
  Primary Magnetizing Current goes Negative for ZVS
  ΔB Same as RCD Clamp
  Design for Core Loss Limit not Saturation Limit
VPRI
VIN=48V
IPRI
IOUT=10A
Q3
Operation
Q3
Q2
Q1
Q4

## Slide 18: UCC2891EVM Clamp Voltage Limits
Vin=36V, Iout=10A
  Dmax=58%
  Vclamp=89V
Vin=72V, Iout=10A
  Dmin=28%
  Vclamp=102V
IPRI
VCL
VGS
IPRI
VCL
VGS

## Slide 19: Transformer Design Considerations
Active Clamp Transformer Considerations
  Turns Ratio Effect on Clamp Voltage (Vds)
  Turns Ratio Effect on SR Gate Drive
For N=6, 36V<VIN<72V:
6V<Vgs(QF)<12
5.5V<Vgs(QR)<8.5V

## Slide 20: UCC2891EVM SR Gate Drive
VIN=36V
VIN=72V
VGS(QF)
VGS(QR)
VGS(QF)
VGS(QR)
VIN | SR | VGS | Rds(ON)
36V | QF | 6.3V | 3.125mΩ
 | QR | 8.4V | 2.75mΩ
72V | QF | 12V | 2.5mΩ
 | QR | 5.4V | 3.25mΩ
Variable VGS = Variable Rds(ON)

## Slide 21: UCC2891EVM Primary Gate Drive
Q6 Must be P-Channel for Low-Side Clamp
Clamp Circuit (C10, D3, R8) Required on Q6
Aux to Out Delay (per side) Set by:
OUT
AUX
TDELAY
Q7 (VGS)
Q6 (VGS)

## Slide 22: UCC2891EVM Q7 ZVS Waveforms
Q7 Turn-On
  11ns VGS, VDS Overlap
  VDS Can’t Resonate to Ground
  Not Enough Inductive Energy
  Not Enough Delay Time
Q7 Turn-Off
  Always ZVS
VCL=VDS
VGS
VCL=VDS
VGS

## Slide 23: Forcing Q7 Turn-On ZVS
Q7 Turn-On (Vin=72V)
  1μH Inductor Added in Series with Transformer Primary
  Increase UCC2891 OUT/AUX Delay Time
  Increased Delay Implies Decreased Max Duty Cycle
  Increase Max Duty Cycle Clamp Can Increase Max VDS Stress
VCL=VDS
TDELAY

## Slide 24: Performance Improvements that can be made on the EVM
Integrated Planar Magnetics
  Reduce Copper Losses
  Optimize Transformer and Inductor Design
Regulated Secondary SR Gate Drive
  Control Driven Verses Self Driven
  UCC27228 Predictive Gate Drive on Secondary for additional Efficiency Gains (UCC27228 is new product due to release Q2 2004)
Optimize ZVS Turn-On of Main MOSFET
  Reduce Turns Ratio (Duty Cycle) to Allow Additional Time for ZVS
  Saturable Reactor Added to Secondary May Help ZVS

## Slide 25: References
Literature
UCC289/1/2/3/4 Current-Mode Active Clamp PWM Controller Datasheet, Texas Instruments Literature No. SLUS542
Active Clamp and Reset Technique Enhances Forward Converter Performance, Power Supply Design Seminar SEM-1000, Topic 3, by Bill Andreycak, Texas Instruments Literature No. SLUP108
Design Considerations for Active Clamp and Reset Technique, Power Supply Design Seminar SEM-1100, Topic 3, by Dhaval Dalal, Texas Instruments Literature No. SLUP112
48-V Input, 3.3V/100 Watt Converter With UCC3580-1 Controller, User guide to Accommodate PMP206_C Reference Design, Texas Instruments Literature No. SLUU146
UCC2891EVM, 48-V to 1.3-V, 30-A Forward Converter with Active Clamp Reset, User Guide to Accommodate UCC2891EVM by Steve Mappus, Texas Instruments Literature No. TBD – Available Q403
Designing for High Efficiency with the UCC289/1/2/3/4 Active Clamp PWM Controller, Application Note by Steve Mappus, Texas Instruments Literature Number TBD – Available Q403
Development Tools
UCC2891EVM, 48-V to 3.3-V, 30-A Forward Converter with Active Clamp Reset, Texas Instruments Development Tool No. UCC2891EVM – Available Q404

## Slide 26: UCC2891 Final Thoughts
Part Differences
  UCC2891/3 for 24-48V isolated input systems
  UCC2892/4 for Off-Line Applications or low input voltage systems below 24Vin
ZVS
  Always Get ZVS at Turn-Off
  Conditional ZVS at Turn-On
UCC2891 Highlights
  High Efficiency
  Loaded With Internal Part Features
  Improved Performance and Features over Competition
  ±2A TrueDrive™ Output Stage
  2891 Eliminates the “Disadvantages” Normally Associated with Active Clamp
Product Released October 30, 2003